## Slide 1: From ARIES to MARS: Transaction Support for Next-Generation, Solid-State Drives
Joel Coburn*, Trevor Bunker*, Meir Schwarz, Rajesh Gupta, Steven Swanson
Non-volatile Systems Laboratory
Department of Computer Science and Engineering
University of California, San Diego
* Now at Google

## Slide 2: Faster than Flash Non-volatile Memories
Spin-torque
MRAM
Phase change memory
Memristor
Flash is everywhere but has its idiosyncrasies
New device characteristics
  Nearly as fast as DRAM
  Nearly as dense as flash
  Non-volatile
  Reliable
Applications
  DRAM replacements
  Fast storage

## Slide 3
Chart: 1/Latency Relative To Disk
| 1 | 104.4117647058824 | 43.292682926829301 | 104.4117647058824 | 865.85365853658539 | 2840 | 5916.6666666666697 | 2958333.3333333302
Latency Improvement | 1 | 100 | 440 | 364 | 640 | 4800 | 7200 | 328000
Hard Drives (2006)
PCIe-Flash (2007)
PCIe-PCM (2010)
PCIe-Flash (2012)
PCIe-PCM (2014?)
DDR Fast NVM (2016?)
5917x  2.4x/yr
7200x  2.4x/yr
More than Moore’s Law Performance

## Slide 4: Realizing the Potential of fast NVMs
Physical Storage
Low-level IO
File System
Process Isolation
Applications
Storage Controller
NV-DIMM
NV-DIMM
NV-DIMM
NV-DIMM
NV-DIMM
NV-DIMM
Low-level IO
File System
Process Isolation
Applications
15
9
8
3
20
20
29
29
20
Log
X
29
WAL algorithms were designed for disk!

## Slide 5: Moneta-Direct SSD for Fast NVMs
FPGA-based prototype
  DDR2 DRAM emulates PCM
  PCIe: 2GB/s, full duplex
Optimized kernel driver and device interface
  Eliminate disk-based bottlenecks in IO stack
User-space driver
  Eliminates OS and FS costs in the common case
5µs latency,
1.8M IOPS for 512B requests
[SC 2010, Micro 2010, ASPLOS 2012]

## Slide 6: Characteristics of Fast SSDs
 | Disk | Moneta
Latency (4KB) | 7000µs | 7µs
Bandwidth (4KB) | 2.6MB/s | 1700MB/s
Sequential/random performance | ~100:1 | 1:1
Minimum request size/alignment | Block | Byte
Parallelism | 1 | 64
Internal/external bandwidth | 1:1 | 8:1

## Slide 7: Existing Support for Transactions
Disk-based systems
  Write-ahead logging approaches: ARIES [TODS 92], Stasis [OSDI 06], Segment-based recovery [VLDB 09], Aether [VLDB 10]
  Device/HW support: Logical Disk [SOSP 93], Atomic Recovery Units [ICDCS 96], Mime [HPL-TR 92]
  Shadow paging in file systems: ZFS, WAFL
Non-volatile main memory
  Persistent regions: RVM [TOCS 94], Rio Vista [SOSP 97]
  Programming support: Mnemosyne, NV-heaps [ASPLOS 11]
Flash-based SSDs
  Transactional Flash [OSDI 08]
  FusionIO’s AtomicWrite [HPCA 11]

## Slide 8: ARIES: Write-Ahead Logging Recovery Algorithm for Databases
Feature | Benefit(s)
Flexible storage management | Supports varying length data and high concurrency
Fine-grained locking | High concurrency
Partial rollbacks via savepoints | Robust and efficient transactions
Recovery independence | Simple and robust recovery
Operation logging | High concurrency lock modes
Fast, flexible, and scalable ACID transactions

## Slide 9: ARIES Disk-Centric Design
Design Decision | Advantages | How?
No-force | Eliminate synchronous random writes | Flush redo log entries to storage on commit
Steal | Reclaim buffer space (scalability) Eliminate random writes Avoid false conflicts on pages | Write undo log entries before writing back dirty pages
Pages | Simplify recovery and buffer management Match the semantics of disk | All updates are to pages Page writes are atomic
Log Sequence Numbers (LSNs) | Simplify recovery Enable features like operation logging | LSNs provide an ordering on updates
Good for disk, not good for fast SSDs

## Slide 10: MARS: Modified ARIES Redesigned for SSDs
Moneta-Direct Driver
Storage Manager
Moneta-Direct SSD
Applications
Kernel IO
File System
Simplified ARIES Replacement
+
Flexible software interface
+
Hardware support
Editable Atomic Writes

## Slide 11: Editable Atomic Writes (EAWs)
Atomic {
Write A
Write B
Write C
…
If(x)
Write A’
…
}
Log
Data
Storage
A
B
C
A’
Write the log
Commit
Applications can access and edit the log prior to commit.
Hardware copies data in-place.

## Slide 12: Editable Atomic Write Execution
A
A
B
C
Storage
Transaction
Table
Metadata
File
B
Log
File
Data
File
Memory
LogWrite(t1,memA,dataA,logA);
LogWrite(t1,memB,dataB,logB);
LogWrite(t1,memC,dataC,logC);
If(x) Write(memA,logA);
Commit(t1);
// WriteBack(t1);
PENDING
C
COMMITTED
FREE
0
63
A
A’
A’
A’
A’
B
C

## Slide 13: Designing MARS for Fast NVMs
No-force
Steal
Pages
LSNs
Perform write backs in hardware at the memory controllers
Hardware does in-place updates
Eliminate undo logging
Log always holds latest copy
Software sees contiguous objects
Hardware manages the layout of objects across memory controllers
Hardware maintains ordering with commit sequence numbers

## Slide 14: MARS Features using EAWs
Feature | Provided by MARS?
Flexible storage management | 
Fine-grained locking | 
Partial rollbacks via savepoints | 
Recovery independence | 
Operation logging | N/A

## Slide 15: EAW Hardware Architecture
8 GB
8 GB
Logger
Ring
Control
Transfer Buffers
DMA
Control
Score
board
Host
via
PIO
Host via
DMA
Req Queue
Ring (4 GB/s)
8 GB
Logger
8 GB
Logger
8 GB
Logger
Logger
8 GB
Logger
8 GB
Logger
8 GB
Logger
TID
Manager
Tag
Renamer
Perm
Check
TID Status
Req Status
2-phase commit protocol
Commit
Pend
Pend
Pend
Comm
Comm
Comm
Write back
Ack
Free
Free
Free

## Slide 16: Latency Breakdown
Up to 3x faster than software only

## Slide 17: Bandwidth Comparison
Chart: Access Size (KB)
| 0.5 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512
Write | 811.2143 | 1370.1662 | 1638.7759 | 1660.19 | 1669.1386 | 1663.4754 | 1674.2769 | 1672.0948 | 1674.8061 | 1672.3644 | 1675.5669
SoftAtomic | 197.1475 | 356.6344 | 546.2614 | 681.8963 | 756.7722 | 789.8089 | 815.0135 | 827.1579 | 832.9669 | 835.9309 | 837.2128
Chart: Access Size (KB)
| 0.5 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512
Write | 811.2143 | 1370.1662 | 1638.7759 | 1660.19 | 1669.1386 | 1663.4754 | 1674.2769 | 1672.0948 | 1674.8061 | 1672.3644 | 1675.5669
AtomicWrite | 742.9279 | 1238.7837 | 1583.8971 | 1642.4761 | 1663.1338 | 1672.0403 | 1672.5858 | 1676.4175 | 1675.2405 | 1675.4022 | 1672.8446
SoftAtomic | 197.1475 | 356.6344 | 546.2614 | 681.8963 | 756.7722 | 789.8089 | 815.0135 | 827.1579 | 832.9669 | 835.9309 | 837.2128
2 to 3.8x
improvement

## Slide 18: Internal Memory Bandwidth
Chart: Access Size (KB)
| 0.5 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512
Write | 813.3914 | 1377.9527 | 1638.733 | 1659.3069 | 1668.7496 | 1673.2936 | 1675.4326 | 1674.2995 | 1675.1256 | 1675.2494 | 1675.6703
AtomicWrite | 2559.3398 | 4150.1974 | 4980.1045 | 5044.9181 | 5048.6379 | 5078.0378 | 5077.2872 | 5097.7849 | 5076.5553 | 5073.144 | 5053.5157
SoftAtomic | 1006.087 | 1253.6303 | 1509.1514 | 1621.9181 | 1659.3209 | 1658.9583 | 1671.0466 | 1676.6915 | 1679.1618 | 1680.3053 | 1680.445
3x bandwidth

## Slide 19: MemcacheDB: Persistent Key Value Store
1.7x faster than SoftAtomic, 3.8x faster than BDB
Chart: Client Threads
| 1 | 2 | 4 | 8
Unsafe | 21685.3414 | 38504.3375 | 64500.7321 | 78573.7297
Editable Atomic Write | 20690.6112 | 35827.5263 | 59389.1235 | 67012.0018
SoftAtomic | 17814.9596 | 29792.4065 | 44772.7782 | 40459.1302
Berkeley DB | 13171.7424 | 20523.5138 | 26715.8952 | 17588.881

## Slide 20: Comparison of MARS and ARIES
4x throughput improvement and better scalability
Chart: Threads
| 1 | 2 | 4 | 8 | 16
4KB-MARS | 21907 | 40880 | 72677 | 117851 | 144201
4KB-ARIES | 16312 | 29036 | 42443 | 42256 | 38776

## Slide 21: Conclusions from MARS
MARS: Redesign of write-ahead logging for NVMs
  Provides the features of ARIES but none of the disk-related overheads in a database storage manager
Editable Atomic Writes (EAWs)
  Makes the log accessible and editable prior to commit
  Minimizes the cost of atomicity and durability
  Offloads logging, commit, and write back to hardware
MARS achieves 4x the performance of ARIES
  Reduces latency and required host/device bandwidth

## Slide 22
Thank you!
Any questions?